## Slide 1: WIFI ROUTER GAMING CONFIG

## Slide 2: 1. Wireless Security
2
- Wireless => Wireless Security
- WPA/WPA2 – Personal => Version => WPA2 – PSK

## Slide 3: 2. Network WAN
3
- Network => Wan
- MTU Size (in bytes) = 1300

## Slide 4: 3. Wireless Advanced
4
- Wireless => Wireless Advanced
- Beacon Interval = 80; RTS Threshold = 1500

## Slide 5: 4. Wireless Setting
5
- Wireless => Wireless Setting
- Channel = 20MHz

## Slide 6: 4. Wireless Setting
6
- Time zone => GMT +7:00
- NTP Server = time1.google.com

## Slide 7
7
Thank you!

## Slide 8: DD-WRT FIRMWARE UPDATE FOR WR TPLINK 841N

## Slide 9: 1. Version WR
9
- Kiểm tra version WR để chọn file firmware update cho phù hợp
- Link download: http://sce.sctv.net.vn/downloads/TPLink/841N/

## Slide 10: 2. Upgrade lần 1
10
- Chọn file “factory-to-ddwrt.bin”
=> “Upgrade”

## Slide 11: 2. Upgrade lần 1
11
=> Cofirm “OK”

## Slide 12: 2. Upgrade lần 1
12
- “Không reset power”.
- Sau 300s thay đổi local IP = 192.168.1.1 để vào giao diện mới của WR
- Account login nếu có = admin/admin

## Slide 13: 2. Upgrade lần 2
13
- Administrator => Firmware Upgrade
- Chọn file “tl-wr841nd-webflash.bin”
=> “Upgrade”

## Slide 14: 2. Upgrade lần 2
14
- Upgrading.

## Slide 15: 2. Upgrade lần 2
15
    - Successful and rebooting.

## Slide 16: 3. Auto Reboot WR
16
Administrator => Management => Cron => Enable

## Slide 17: 3. Auto Reboot WR
17
- Administrator => Keep Alive => Schedule Reboot => Enable
- At a set Time => chọn thời điểm và chu kì Reboot.

## Slide 18
18
Thank you!